MINIJUKE BASIC INSTRUCTIONS

TO HOOK UP THE MINIJUKE LEADS, THE 5 METRE LEADS HAVE A 3 PIN POWER PLUG + FEMALE AUDIO PLUG AT ONE END. THIS CONNECTS TO THE BACK OF THE MINIJUKE, THERE IS A 3 PIN POWER SOCKET + AUDIO INPUT SOCKET ON THE BACK, PLUG THESE INTO HERE, IT DOES NOT MATTER WHICH WAY AROUND THE AUDIO PLUG IS, THEY CAN PLUG INTO EITHER SOCKET.

ON THE OTHER END IS A POWER PLUG + MALE AUDIO PLUG, THE POWER PLUG CONNECTS TO THE POWER SOCKET ON THE SPEAKER AND THE MALE AUDIO PLUG GOES INTO THE MIDDLE LINE INPUT SOCKET ON THE BACK OF THE SPEAKER. MAKE SURE THE POWER BUTTON ON THE SPEAKER IS SWITCHED TO ON.

CONNECT THE MINIJUKE POWER PLUG ON THE BACK, TO THE MAINS AND TURN ON THE MACHINE VIA THE ON BUTTON ON THE BACK, EVERYTHING SHOULD BE ALL GO AND WAIT FOR THE SOFTWARE TO LOAD.

TO USE THE MIXER ON THE SIDE YOU WILL NEED TO TURN ON THE POWER BUTTON, MAINLY USED IN CONJUNCTION WITH A MICROPHONE FOR SPEECHES OR KARAOKE USE. IF YOU ARE NOT USING A MICROPHONE FOR ANYTHING THEN LEAVE THE MIXER OFF. THE MIXER HAS TONE/ECHO CONTROL AND 2 X MICROPHONE INPUT SOCKETS WITH SEPERATE VOLUME CONTROLS FOR EACH MICROPHONE.

NOTE  USING A MICROPHONE TO CLOSE TO A SPEAKER CAN CAUSE HIGH-PITCHED FEEDBACK, TO AVOID THIS MOVE SPEAKERS AWAY AS AFR AS YOU CAN FROM THE MINIJUKE UNIT. TO GET MORE VOLUME FOR KARAOKE LIFT THE VOLUME UP ON THE ONSCREEN CONTROLS FIRST THEN ADJUST THE MICROPHONE LEVEL VOLUME TO SUIT.

FOR OPERATION OF THE SOFTWARE USE THE PANEL IN THE RIGHT HAND CORNER, IT IS SELF-EXPLAINATORY.

TO GET INTO PLAY CONTROL USE THE CODE 747 THEN PUSH ENTER. GO TO CREATE PLAYLIST (RHS) PICK A LIST FROM 1 – 9 CLEAR OUT ANY EXISTING LIST AND FOLLOW ON SCREEN INSTRUCTIONS.

IF SELECTION LOCKED, TO UNLOCK IT USE THE CODE 681 THEN PUSH ENTER.